## Slide 1: Introduction to Sensors & Actuators for IoT

## Slide 2: What are sensors
A Sensor is a device that detect a change in the surrounding and transform it into another form (Say into an electrical pulse, or an action). However it should in no way impact the environment and change the change the process which is causing the temperature
A sensor can be electronic, mechanical, electrical or anything…

## Slide 3: what are sensor for IoT
A Sensor that can measure the change in environment and transform into electrical signal that represent the measurement.
Example:
A temperature sensor can measure the current temperature in the room. Or the temperature of the liquid in which it is dipped or Temperature of the surface which is in contact.
A Sensor is a device that detect a change in the surrounding and transform it into another form (Say into an electrical pulse, or an action). However a sensor should in no way impact the environment and change or influence the process which is causing the change.

## Slide 4: Let us take the design of simple temperature sensor take the discussion forward

## Slide 5: Background of sensors
Sensors existed much before days of electronics and computers. Those days they played a dual role of taking the measurement as well turning that into a action.
Bimetalic stirp used in tradtional iron boxes are a good example of mechanical sensor. This was heavily used in many equipment for temperature control

## Slide 6
Bimetaloc strip was invented by… John Harrison, an eighteenth-century clockmaker who made it for his third marine chronometer (H3) of 1759 to compensate for temperature-induced changes in the balance spring.
Harrison's solution revolutionized navigation and greatly increased the safety of long-distance sea travel.

## Slide 7: Can we build a sensor of our own ?
Many of the sensors which were used in industries where manually build. Semiconductor sensors which arrived lately has some advantages over the manually build one.
A simple temperature sensor can be build with a few meters of copper wire. Here the variation of electrical resistance in metal is used to measure temperature.
Resistance thermometers, are build using this kind of sensor. (RTD Resistance Temperature Detectors)
Yes it is possible to build sensors of your own

## Slide 8: Another way to measure Temperature
Metal Wire – A
Metal Wire – B
Hot Junction
Cold Junction
Voltage Proporational to difference in Temperature

## Slide 9: Comparison on RTD with Thermocouple
No | Advantages | Disadvantages
1 | The thermocouple is less expensive than RTD. | The stray voltage pick up is possible
2 | It has wide temperature ranges and good reproducibility, It has rugged construction | As output voltage is very small, it needs amplification.
3 | The temperature range is 270 to 2700 degree Celsius | The cold junction and lead compensation is essential.
4 | It does not required bridge circuit. | It shows non linearity.
5 | It has good accuracy. | 
6 | It has high speed of response. | 
7 | No self heating | 

## Slide 10: To read more …
1.https://www.ti.com/lit/an/sbaa274/sbaa274.pdf?ts=1595152129802&ref_url=https%253A%252F%252ww
w.google.com%252F

## Slide 11: Diode as a temperature sensor

## Slide 12: DHT-11 Temperature sensor
The DHT11 is a basic, digital temperature and humidity sensor. It uses a capacitive humidity sensor and a thermistor to measure the surrounding air, and gives out a digital signal on the data pin (no analog input pins needed). It is simple to use, but requires careful timing to grab data. The only real downside of this sensor is you can only get new data from it once every 2 seconds, so when using the library, sensor readings can be up to 2 seconds old.

## Slide 13
Power from a USB
Mobile charger

## Slide 15
#include "DHT.h"
#define DHTPIN 4
#define DHTTYPE DHT11
DHT dht(DHTPIN, DHTTYPE);
void loop()
{
// Wait a few seconds between measurements.
delay(2000);
float h = dht.readHumidity();
float c = dht.readTemperature();
// Check if any reads failed and exit early (to try again).
if (isnan(h) || isnan(t) || isnan(f))
{
Serial.println(F("Failed to read from DHT sensor!"));
return;
}
float hic = dht.computeHeatIndex(t, h, false);
Serial.print(F("Humidity: "));
Serial.print(h);
Serial.print(c);
Serial.print(F("°C "));
Serial.print(F("°F Heat index: "));
Serial.print(hic);
Serial.print(F("°C "));
}

## Slide 16: Infrared Thermometer
http://www.esp32learning.com/code/esp32-and-mlx90614-infrared-thermometer-example.php

## Slide 17: What are sensor for IOT
Practically any sensor can be used for IOT application provided the sensor can give a Digital output. In case the sensor provides only an analog output. In which we need to provide a Digital to Analog convertor.

## Slide 18: What cannot be used with IOT
When there
Was NO RPM sensors available This was the only option.

## Slide 19: Nature of sensors
NO | Sensor Use
1 | Temperature and Humudity
2 | Water Turbidity sensor
3 | Air quality(Co2, methane, etc)
4 | Dust Sensor
5 | Current Sensor
6 | pH and TDS sensor
7 | Optical Sensor
8 | Magnetic field sensors / Hall effect sensors
9 | Vibration Sensor
10 | Electronic Gyroscope
NO | Sensor Use
11 | RPM Sensor
12 | Water Pressure Sensor
13 | Weight Sensor
14 | Proximity sensor
15 | Wind speed sensor
16 | GPS
17 | Heart Beat and SPO2 sensor
18 | Tilt sensor
19 | Gas leakage sensor
20 | Touch sensor

## Slide 20: What are Actuators
An actuator is a component of a machine that is responsible for moving and controlling a mechanism or system, for example by opening a valve. In simple terms, it is a "mover".
Actuator
Energy/ Power Supply
Control Signal (from a computer)
Mechanical Force or an action

## Slide 21: How does a very simple actuator works
Neutral
Phase

## Slide 22
const int relay = 26;
void setup()
{
Serial.begin(115200);
pinMode(relay, OUTPUT);
}
void loop()
{
// Normally Open configuration, send LOW signal to let current flow
// (if you're usong Normally Closed configuration send HIGH signal)
digitalWrite(relay, LOW);
Serial.println("Current Flowing");
delay(5000);
// Normally Open configuration, send HIGH signal stop current flow
// (if you're usong Normally Closed configuration send LOW signal)
digitalWrite(relay, HIGH);
Serial.println("Current not Flowing");
delay(5000);
}

## Slide 23: How do we make this as Iot Device in the field
Let us see how to control the pump set through internet
Public
Internet

## Slide 24: Big Picture
Public Internet

## Slide 25
Run a WEB SERVER in the ESP32 Board
Access the web server from home through a mobile/laptop
Web server has direct access to GPIO ports on ESP32
Now by using WEB, we control the Pump set

## Slide 26
Let us Review the code

## Slide 27: Challenges
Farm Network
(wifi at Farm)
Home network
(Wifi at home)
Public
Internet

## Slide 28: Challenges-2
The user does not know what is the happening in the farm
There is no way to know the pump is really running or not
There is no way to know whether there is water in the source
There is no way to know whether farm is over flowing or nor
The climate at Farm
Other issues